## Slide 1: UART Nick Mould Fall 2016

## Slide 2: UART (Universal Asynchronous Receiver Transmitter)
The UART circuit transmits and receives serial data (1 bit at a time, or one bit per clock cycle)
Communication systems can be half-duplex or full-duplex.
  Half duplex: both communication devices take turns transmitting and receiving (old)
  Full duplex: both communication devices transmit and receive simultaneously (pretty much everything)

## Slide 3: More UART
UART Examples:
  RS232, 1969, Low: [-3V, 15V], High: [-15V, 3V]
  RS422, 1994, Differential Pair: [-6V, 6V]
  RS485, 1998, Differential Pair: [a,b] s.t. |a-b| > 200mV
  RS (Recommended Standard)
  TIA (Telecommunications Industry Alliance)
  EIA (Electronic Industries Alliance)
  Read Wikipedia for more history

## Slide 4: More UART
All of the different UART standards define different signals that will be used to communicate between the 2 devices.
The most important signals are the Tx (transmit) and the Rx (receive)
The old RS232 had weird signals such as:
  RTS (Request to send)
  DTR (Data terminal ready)
  CTS (Clear to Send)
Why?

## Slide 5: More UART
We will consider the UART to be composed of 2 independent transmit and receive circuits.
Let us examine the UART data format:
  Start Bit, Must be 1 bit
  Data, Usually 8 bits
  Parity Bit, Optional, not used very often
  Stop Bits(s), Usually 1 bit
The 8N1 UART will be our focus.
  8 data bits
  No parity bits
  1 stop bit
  The 1 start bit is implied

## Slide 6: More UART (Receive)
We expect to receive data in this order:
  1 start bit, 8 data bits, and 1 stop bit
  10 bits at a time
The challenge with the UART is that there is no shared clock.
We will essentially have one input to our receive circuit: The Rx signal.
We will monitor the Rx signal with a state machine.
  The signal will be high by default
  When the signal goes low, THAT’S THE START BIT
  After we receive the start bit we go to a different state and shift in the 8 data bits.
  The stop bit will be HIGH.

## Slide 7: More UART (Receive)
How fast do we run our state machine?
  We need to go the same speed as the other device that is transmitting bits to our device.
  A Clock speed is agreed upon between the two devices.
The last problem: The transmit and receive clocks are not synchronized. We need to examine this problem with a diagram.
Draw a timing diagram.

## Slide 8: More UART (Receive)
Solution: Use a clock that is much faster than the Rx data to monitor the Rx signal.
  For example: drive the state machine with a clock that is 100 times faster than the Rx data.
  When the start bit goes low, count 50 clock ticks before changing states to read the data.
  In the data read state count to 100 before shifting the data into a receive register.
  Basically, try to read the data bits on the Rx signal in the middle of their hold time.

## Slide 9: More UART (Transmit)
Shift out 10 bits of data: 1 start bit, 8 data bits, and 1 stop bit.
Receiving these bits is someone else’s problem.
Make sure to do this at the appropriate clock frequency (whatever frequency the receiver expects).

## Slide 10: More UART (FIFOs)
When we transmit the data has to come from somewhere.
When we receive, we have to put the data somewhere.
Usually the data will be many bytes.
We will use FIFOs.
Draw diagram.

## Slide 11: FIFO (First In First Out)
FIFOs are heavily used in digital design.
A FIFO is a big fancy shift register.
What signals are associated with a FIFO?
  Data In
  Write Enable
  Write Clock
  Full
  Data Out
  Read Enable
  Read Clock
  Empty